## Slide 1
Metering Valve
Avionics
BSCU
Blue
Hydraulic Pump
Hydraulic Pressure
Wheel Speed
Braking Pedal
Mechanical Pedal Position
Hydraulic Pressure
(Reserve)
Accumulator
Anti-Skid Valve
Hydraulic Pressure
Selector Valve
Hydraulic Pressure
Shutoff Valve
Metering Valve
Green
Hydraulic Pump
Hydraulic Pressure
Hydraulic Pressure
Hydraulic Pressure
Anti-Skid Command
Braking Command
Braking Command

## Slide 2: Metering Valve
Init
Exec
S1
S2
MeterHyd := 0
receiveASHyd(AntiSkidHyd)
R1
R2
receiveBRKCMD(BrakingCMD)
receiveMechCMD(MechanicalCMD)
①
②
Variable | type | Input/Output
AntiSkidHyd | Enumeration | Input
BrakingCMD | Boolean | Input
MechanicalCMD | Boolean | Input
MeterHyd | Enumeration | Output
Transition | Guard | Action
1 | BrakingCMD ¦ MechanicalCMD == true | MeterHyd:=AntiSkidHyd
2 | BrakingCMD ¦ MechanicalCMD == false | MeterHyd:=0
Function: control pressure to the demanded level and to provide regulation for the Anti-Skid function.
Behavior: Inherit hydraulic pressure from Anti-Skid module when there exists at least a TRUE value among Braking command & Mechanical command.
sendMeterHyd(MeterHyd)
sendMeterHyd(MeterHyd)

## Slide 3
Init
Exec
S1
S2
AntiSkidHyd := 0
receiveSOHyd(ShutOffHyd)
R1
R2
receiveAccHyd(AccumulatorHyd)
receiveASCMD(AntiSkidCMD)
①
②
Variable | type | Input/Output
ShutOffHyd | Enumeration | Input
AccumulatorHyd | Enumeration | Input
AntiSkidCMD | Boolean | Input
AntiSkidHyd | Enumeration | Output
Transition | Guard | Action
1 | ASCMD == true | AntiSkidHyd:=ShutOffHyd + AccumulatorHyd
2 | ASCMD== false | AntiSkidHyd:=0
Function: restrict the hydraulic line pressure to the brakes in order to prevent locking of the wheels.
Behavior: Inherit hydraulic pressure from Shut Off or Accumulator module when Anti-Skid command is TRUE.
sendASHyd(AntiSkidHyd)
sendASHyd(AntiSkidHyd)
Anti-Skid Valve

## Slide 4: Shutoff Valve
Init
Exec
S1
S2
ShutOffHyd := 0
R1
receiveHydraulic(Hydraulic)
①
②
Variable | type | Input/Output
Hydraulic | Enumeration | Input
ShutOffCMD | Boolean | Input
ShutOffHyd | Enumeration | Output
Transition | Guard | Action
1 | SOCMD == true | ShutOffHyd:=Hydraulic
2 | SOCMD== false | ShutOffHyd:=0
Function: respond to commands from the BSCU to apply hydraulic pressure to the braking discs.
Behavior: Inherit hydraulic pressure from Hydraulic Pump module when Shutoff command is TRUE.
sendSOHyd(ShutOffHyd)
sendSOHyd(ShutOffHyd)
receiveSOCMD(ShutOffCMD)

## Slide 5: Hydraulic Pump
Variable | type | Input/Output
Hydraulic | Enumeration | Output
Function: provide hydraulic pressure to the system.
Behavior: Maintain a positive hydraulic pressure out for the system.
Exec
sendHydraulic(Hydraulic)
Hydraulic := 10
Notice: The green/blue hydraulic pump use the same component model in current design.

## Slide 6: Accumulator
Variable | type | Input/Output
Hydraulic | Enumeration | Output
Function: provide enough pressure to apply pressure for the required number of presses of the braking pedal and supply pressure to the parking brake as well.
Behavior: Maintain a positive hydraulic pressure out for the system.
Exec
Hydraulic := 10
sendAccHyd(AccumulatorHyd)

## Slide 7: Parking Brake
Variable | type | Input/Output
Handle | Boolean | Input
Brake | Boolean | Input
ClampingForce | Boolean | Output
Transition | Guard | Action
1 | Brake == true ¦¦ Brake == off & Handle == false | ClampingForce:=false
2 | Brake == true ¦¦ Brake == off & Handle == true | ClampingForce:=true
3 | Brake == false & Handle == false | ClampingForce:=true
4 | Brake == false & Handle == true | ClampingForce:=false
Function: The parking brake handle will be used to set the parking brake system. To set the parking brake, the brake pedals must be fully depressed. The parking brake handle can then be pulled up and will latch when the pedals are released. The brake system will maintain brake clamping force without further flight crew action once the parking brake has been set. The brake pedals must be depressed to unlatch the parking brake handle.
Up
Down
①
②
③
④

## Slide 8: BSCU
Transition | Guard | Action
1 | null | receiveSpeed(WheelSpeed)
2 | null | receivePedal(PedalPosition)
3 | PedalPostion != 0 | ShutOffCMD := true
4 | PedalPosition == 0 | ShutOffCMD := false
Function: The brake pedal position is electrically fed to a braking computer. This in turn produces corresponding control signals to the brakes. In addition, this computer monitors various signals which denote certain critical aircraft and system states, to provide correct brake functions and improve system fault tolerance, and generates warnings, indications and maintenance information to other systems. This computer is accordingly named the Braking System Control Unit (BSCU).
Exec1
R2
P1
P2
Exec2
AS1
AS2
R1
Variable | type | Input/Output
WheelSpeed | Enumeration | Input
PedalPosition | Enumeration | Input
BrakingCMD | Boolean | Output
ShutOffCMD | Boolean | Output
AntiSkidCMD | Boolean | Output
BrakingCMD := true; ShutOffCMD := false; BrakingCMD := false
①
②
③
④
⑤
⑥
⑦
⑧
sendASCMD(AntiSkidCMD)
sendASCMD(AntiSkidCMD)

## Slide 9: BSCU
Transition | Guard | Action
5 | null | snedSOCMD(ShutOffCMD)
6 | null | sendSOCMD(ShutOffCMD)
7 | WheelSpeed > 8 | AntiSkidCMD := false
8 | WheelSpeed <= 8 | AntiSkidCMD := true
Function: The brake pedal position is electrically fed to a braking computer. This in turn produces corresponding control signals to the brakes. In addition, this computer monitors various signals which denote certain critical aircraft and system states, to provide correct brake functions and improve system fault tolerance, and generates warnings, indications and maintenance information to other systems. This computer is accordingly named the Braking System Control Unit (BSCU).
Exec1
R2
P1
P2
Exec2
AS1
AS2
R1
Variable | type | Input/Output
WheelSpeed | Enumeration | Input
PedalPosition | Enumeration | Input
BrakeCMD | Boolean | Output
ShutOffCMD | Boolean | Output
AntiSkidCMD | Boolean | Output
BrakeCMD := true; ShutOffCMD := false; BrakingCMD := false
①
②
③
④
⑤
⑥
⑦
⑧
sendASCMD(AntiSkidCMD)
sendASCMD(AntiSkidCMD)

## Slide 10: Selector Valve
Init
Exec
S1
S2
GreenHydraulicOut := 0
BlueHydraulicOut := 0
R1
receiveGreenHyd
(GreenHydraulicIn)
①
②
Function: respond to commands from the BSCU to apply hydraulic pressure to other valves.
Behavior: Inherit hydraulic pressure from green and blue lines and provide hydraulic pressure to the correspond valve in either of the two line.
receiveSYSVal
(SystemValidity)
R2
receiveBlueHyd
(BlueHydraulicIn)
Variable | type | Input/Output
SystemValidity | Boolean | Input
GreenHydraulicIn | Enumeration | Input
BlueHydraulicIn | Enumeration | Input
GreenHydraulicOut | Enumeration | Output
BlueHydraulicOut | Enumeration | Output
Transition | Guard | Action
1 | SystemValidity & GreenHydraulicIn > 0 | GreenHydraulicOut := GreenHydraulicIn; BlueHydraulicOut := 0
2 | (!SystemValidity ¦ GreenHydraulicIn == 0) & BlueHydraulic > 0 | BlueHydraulicOut := BlueHydraulicIn; GreenHydraulicOut := 0
S3
sendBlueHyd
(BlueHydraulicOut)
sendBlueHyd
(BlueHydraulicOut)
sendGreenHyd
(GreenHydraulicOut)

## Slide 11: Anti-Skid Valve
Init
Exec
S1
S2
AntiSkidHydraulic := 0
R1
receiveHydraulic
(Hydraulic)
①
②
Function: The Anti-Skid Valves will follow BSCU commands to control hydraulic pressure to the braking pads. These valves are used to restrict the hydraulic line pressure to the brakes in order to prevent locking of the wheels. The anti-skid system prevents wheel skids. It optimizes braking by reducing brake pressure when the pilot or autobrake system meters pressure in excess of that required to skid the tires
sendASHyd
(AntiSkidHydraulic)
receiveASCmd
(AntiSkidCmd)
Transition | Guard | Action
1 | AntiSkidCmd <= Hydraulic | AntiSkidHydraulic := AntiSkidCmd
2 | AntiSkidCmd > Hydraulic | AntiSkidHydraulic := Hydraulic
sendASHyd
(AntiSkidHydraulic)
Variable | type | Input/Output
AntiSkidCmd | Enumeration | Input
Hydraulic | Enumeration | Input
AntiSkidHydraulic | Enumeration | Output
The red bolder part can be replaced by……

## Slide 12: Anti-Skid Valve
Init
Exec
AntiSkidHydraulic := 0
R1
receiveHydraulic
(Hydraulic)
sendASHyd
(AntiSkidHydraulic)
receiveASCmd
(AntiSkidCmd)
Transition | Guard | Action
1 | null | AntiSkidHydraulic := min(AntiSkidCmd, Hydraulic)
Variable | Type | Input/Output
AntiSkidCmd | Enumeration | Input
Hydraulic | Enumeration | Input
AntiSkidHydraulic | Enumeration | Output
S1
①
Function: The Anti-Skid Valves will follow BSCU commands to control hydraulic pressure to the braking pads. These valves are used to restrict the hydraulic line pressure to the brakes in order to prevent locking of the wheels. The anti-skid system prevents wheel skids. It optimizes braking by reducing brake pressure when the pilot or autobrake system meters pressure in excess of that required to skid the tires

## Slide 13: Wheel
Init
Exec
WheelPressure := 0
receiveMeterHyd
(GreenMeterHydraulic. BlueMeterHydraulic)
Function: Receive hydraulic pressure from both blue and green line, then choose one of the activated line’s pressure as wheel brake pressure
sendWheelPressure
(WheelPressure)
Transition | Guard | Action
1 | null | WheelPressure := GreenMeterHydraulic + BlueMeterHydraulic
Variable | Type | Input/Output
WheelPressure | Enumeration | Output
GreenMeter Hydraulic | Enumeration | Input
BlueMeter Hydraulic | Enumeration | Input
S1
①